## Slide 1
Motivation:
To automatically display changes in Wireless Sensor Network (WSN) to the web.
Objectives:
Current Wireless Sensor Network can be seen and queried from any browser.
Perform lab tests, by turning sensor nodes on and off.
A portion of Adaptive Sensor Web Language (SWL) grammar
…
15. RequestAnnounce ::= {Identifier .ga();}
16. Response ::= ResponseConstructor | ResponseArrayCon |
ResponseArrayValue | ResponseConfig |
ResponseAnnounce
17. ReponseConstructor ::= {Identifier.IdRest ([Param ]);}
18. ResponseArrayCon ::= {ArrayRef.IdRest ([Param ]);}
19. ResponseValue ::= {Identifier.IdRest = Exp ;}
20. ResponseConfig ::= {Configuration {{varDecl }* {Exp }*}}
21. ResponseAnnounce ::= {nid={Hexdigit}+16;lt={N|S}deg,min,sec
;s={IntegerType};ln={E|W } deg,min,sec
;n={IntegerType}(;SID={Hexdigit +})} |
{NodeConfig }
22. NodeConfig ::= {Configuration{{varDecl}*{Exp }*}}
...
49. deg ::= {Digit }+2
50. min ::= {Digit }+2
51. sec ::= {Digit}+5
…
Sensor Web Language for Dynamic Sensor Networks
Gunita Saini and Bradford G. Nickerson
University of New Brunswick, Faculty of Computer Science
Sensor Web Components – Dynamic Communication
Communication between the web browser, base station and a new sensor node in Wireless Sensor Network (WSN), sequence diagram
ResponseAnnounce message payload - 22 bytes, total size of the ResponseAnnounce message is 28 bytes sent from the sensor node to the base station.
UUID is the Universally unique identifier, unique
throughout the SWL. n is the total number of sensors
attached to the node. Message size of ResponseAnnounce
message is 3+n.
Sample SWL Browser screen
Internet
New Node
gateway(s)
sensor network
Tier 1
Wireless transit
network
Tier 3
base
station
Tier 4
clients
database
Node already
In the WSN
Tier 2
SWL Msg
SWL Msg
SWL Msg
Sensor Node, s1
Base station
Web
Browser
New node s1, starts communication with the gateway and the base station
S1.t()
S1 unknown,
Request Announce
S1.ga()
Response
Announce()
Ack()
Send network
Sent the latest network
Send network
Sent the latest network,
with new node s1
SWL Msg
Wireless Communication
A New Node with
4 sensors attached
New Node starts sending
SWL Msg to the base station
via gateway or a nearby
node already in WSN.
2. Base station sending
RequestAnnounce msg. to
the new node in WSN via
the gateway
3. Node sending
ResponseAnnounce
message to the base station.
Wired
Communication
4. ResponseAnnounce+ sent by the base station to the web browser
NodeUUID
Node Latitude
Node Longitude
Sensor UUID1
…
Sensor UUIDn
Session ID
n
Sample format of ResponseAnnounce message
response{
nid=46f52dc76c6042319;
lt=N45,94,599999;s=97;
ln=W66,63,339128;n=3;
SID=c6cf046dc1fa4e638;
SID=cfdf449efd554fe0b;
SID=391e816927484bcbb;
}
Sent from the new node in WSN and collected by the base station.
Proposed Sensor Observation Service (SOS) interface with Dynamic SWL
Triangle represents a sensor node, circles represent the sensor(s) attached to the node and rectangle represents the gateway.
SOS Consumer
SOS
Messages
SWL
Browser
Database
SWL Server
SOS Messages
SWL
Messages
SOS
Sponsored By: