## Slide 1
Motivation:
Growth of applications depending on position information.
UWB can provide inexpensive, wireless, indoor positioning with decimeter precision.
IEEE 802.15.4-2011 standard is a solid base for widespread real-time location services.
UWB positioning systems lose accuracy in non line of sight (NLOS) conditions.
Ultra WideBand (UWB) real time positioning
Mohammadreza Yavari and Bradford G. Nickerson
University of New Brunswick, Faculty of Computer Science
IEEE 802.15.4-2011, SDS-TW-TOA ranging protocol1
Ranging protocol
Technology
Decawave EVK100 evaluation kit.
Accuracy in LOS : 10 cm
IEEE 802.15.4-2011 compliant
Range : up to 290 m
Dimension : 7 cm by 7 cm
Communication rate : 6.8 Mb/s
Inertial Navigation Unit (IMU) Digital Combo Board - 6 Degrees of Freedom
Gyroscope : ITG3200
Accelerometer : ADXL345
Dimension : 1.52 cm by 1.65 cm
Kalman Filter
UWB system
Range Estimate
NLOS error mitigation
INS system
Acceleration
Orientation
Feedback
Position
System architecture
Objectives
How much is the accuracy of Decawave UWB positioning in LOS/NLOS condition?
Is it possible to have a communication channel simultaneous with positioning? If yes, how much is the maximum communication rate?
How much can NLOS error be mitigated by methods proposed in the literature?
How much can inertial measurement unit (IMU) and Kalman filter increase the LOS/NLOS accuracy of UWB systems ?
What is the minimum number and arrangement of UWB base stations required for accurate positioning, and how does one find this?
www.sparkfun.com
Methodology
Line follower robot with infrared (IR) blocker plate detects actual position in real time.
1- I. G. Zafer Sahinoglu, Sinan Gezici. Ultra-wideband Positioning Systems: Theoretical
Limits, Ranging Algorithms, and Protocols