## Slide 1
Improved Synthesis and Simulation for FPGAs
ODIN II for VTR 8.0 and Beyond
Field-Programmable Gate Arrays (FPGAs)
Flexible and re-programmable hardware.
It is composed of:
  Logic Elements
  Routing elements: Interconnects and Input/Output pins
Verilog-to-Routing (VTR) FPGA CAD Toolset
Turns Synthesizable Verilog Hardware Description Language (HDL) into Routable Circuitry
Improving ABC Logic Optimization and Technology Mapping
We updated the source from ~2012 ABC to ~2018 ABC.
Significant Gains in several important metrics:
Multi-Clock and Clock Domain Support for
Synthesis, Simulation and Optimization
ABC optimizer does not support more than a single clock domain.
How do we fix this?
We iterate through and expose one clock domain at a time to the ABC optimizer by blackbox all the other domains.
Multi-threaded Simulation Optimization
Improve the multi-threaded circuit simulation via:
Inter-cycle parallelism
Intra-cycle parallelism
Memory dictionaries
Aaron G. Graham, Jean-Philippe Legault,
Maria Patrou, Kenneth B. Kent
Faculty of Computer Science, University of New Brunswick
{aaron.graham, jlegault, maria.patrou & ken}@unb.ca
Chart: Ratio of Geometric Means [GEOMEAN(new/old)]
| num_pre_packed_nets | num_pre_packed_blocks | num_post_packed_nets | num_post_packed_blocks | num_clb | num_io | num_outputs | num_memories | num_mult | min_chan_width | critical_path_delay | pack_time | place_time | crit_path_route_time | min_chan_width_route_time
ratio of Geometric Means GEOMEAN(new/old) Geometric Mean | 0.85657 | 0.86613 | 0.90633 | 0.93695 | 0.82782 | 0.99394 | 1 | 0.99971 | 1.0071 | 0.93475 | 0.99212 | 0.80902 | 0.86481 | 0.79453 | 0.82117