## Slide 1
﻿Collaborative Content Distribution in 5G Mobile Networks with Edge Caching
Haoru Xing and Wei Song
Faculty of Computer Science, University of New Brunswick, Fredericton, Canada
CONCLUSION
ABSTRACT
FRAMEWORK
RESULTS
CONTEXT-AWARE SOLUTION
﻿While the fifth-generation (5G) mobile networks are evolving to a content-centric paradigm, the surging traffic demands keep stressing the ever-increasing network capacities. In-network caching and particularly edge caching offer an effective means to alleviate the traffic pressure by saving bandwidth utilization.﻿ We propose an integrated framework, which employs in-network caching at the network edge as well as the mobile core and enables collaboration among virtualized source points in different domains. ﻿The simulation results demonstrate the significant performance improvement of the context-aware solution over traditional approaches in terms of network dynamics and user context exploitation thus relieve network congestion.
We proposed an integrated content distribution framework that leverages cutting-edge technologies such as MEC, NFC and SDN to utilize universal in-network caching and enable collaboration across domains. Furthermore, a case study is conducted to deploy a context-aware video delivery solution over the framework. The simulation results validate the effectiveness of the context-aware solution.
﻿Fig. 1. Integrated framework.
﻿﻿Fig. 1 shows an integrated framework that efficiently integrates the caching capabilities at the mobile core, BSs and mobile devices. Comparing to the traditional LTE model in Fig. 2, it involves extensive cooperation between edge caching and core caching, ﻿considers virtualized sources, and ﻿exploits fine-grained dynamic context information.
﻿Fig. 3. Network topology.
﻿Our context-aware approach makes good use of collaborative in-network caching to optimize content delivery through the network. ﻿We use the approximation algorithm to solve problem﻿. Multiple sources can be selected to fulfill a request and route the video traffic over multiple alternative paths for load balancing. Solution is tested in network topology that shown in Fig. 3.
﻿Fig. 2. ﻿Example of video content distribution through an LTE network.
﻿Fig. 4. Maximum link utilization.
﻿Fig. 5. Variation of target buffer time.